## Slide 1
Chapter 1
Fundamentals of Quantitative Design and Analysis
Computer Architecture
A Quantitative Approach, Sixth Edition

## Slide 2: Computer Technology
Performance improvements:
  Improvements in semiconductor technology
    Feature size, clock speed
  Improvements in computer architectures
    Enabled by HLL compilers, UNIX
    Lead to RISC architectures
  Together have enabled:
    Lightweight computers
    Productivity-based managed/interpreted programming languages
Introduction

## Slide 3: Single Processor Performance
Introduction

## Slide 4: Current Trends in Architecture
Cannot continue to leverage Instruction-Level parallelism (ILP)
  Single processor performance improvement ended in 2003
New models for performance:
  Data-level parallelism (DLP)
  Thread-level parallelism (TLP)
  Request-level parallelism (RLP)
These require explicit restructuring of the application
Introduction

## Slide 5: Classes of Computers
Personal Mobile Device (PMD)
  e.g. start phones, tablet computers
  Emphasis on energy efficiency and real-time
Desktop Computing
  Emphasis on price-performance
Servers
  Emphasis on availability, scalability, throughput
Clusters / Warehouse Scale Computers
  Used for “Software as a Service (SaaS)”
  Emphasis on availability and price-performance
  Sub-class: Supercomputers, emphasis: floating-point performance and fast internal networks
Internet of Things/Embedded Computers
  Emphasis: price
Classes of Computers

## Slide 6: Parallelism
Classes of parallelism in applications:
  Data-Level Parallelism (DLP)
  Task-Level Parallelism (TLP)
Classes of architectural parallelism:
  Instruction-Level Parallelism (ILP)
  Vector architectures/Graphic Processor Units (GPUs)
  Thread-Level Parallelism
  Request-Level Parallelism
Classes of Computers

## Slide 7: Flynn’s Taxonomy
Single instruction stream, single data stream (SISD)
Single instruction stream, multiple data streams (SIMD)
  Vector architectures
  Multimedia extensions
  Graphics processor units
Multiple instruction streams, single data stream (MISD)
  No commercial implementation
Multiple instruction streams, multiple data streams (MIMD)
  Tightly-coupled MIMD
  Loosely-coupled MIMD
Classes of Computers

## Slide 8: Defining Computer Architecture
“Old” view of computer architecture:
  Instruction Set Architecture (ISA) design
  i.e. decisions regarding:
    registers, memory addressing, addressing modes, instruction operands, available operations, control flow instructions, instruction encoding
“Real” computer architecture:
  Specific requirements of the target machine
  Design to maximize performance within constraints: cost, power, and availability
  Includes ISA, microarchitecture, hardware
Defining Computer Architecture

## Slide 9: Instruction Set Architecture
Class of ISA
  General-purpose registers
  Register-memory vs load-store
RISC-V registers
  32 g.p., 32 f.p.
Defining Computer Architecture
Register | Name | Use | Saver
x0 | zero | constant 0 | n/a
x1 | ra | return addr | caller
x2 | sp | stack ptr | callee
x3 | gp | gbl ptr | 
x4 | tp | thread ptr | 
x5-x7 | t0-t2 | temporaries | caller
x8 | s0/fp | saved/ frame ptr | callee
Register | Name | Use | Saver
x9 | s1 | saved | callee
x10-x17 | a0-a7 | arguments | caller
x18-x27 | s2-s11 | saved | callee
x28-x31 | t3-t6 | temporaries | caller
f0-f7 | ft0-ft7 | FP temps | caller
f8-f9 | fs0-fs1 | FP saved | callee
f10-f17 | fa0-fa7 | FP arguments | callee
f18-f27 | fs2-fs21 | FP saved | callee
f28-f31 | ft8-ft11 | FP temps | caller

## Slide 10: Instruction Set Architecture
Memory addressing
  RISC-V: byte addressed, aligned accesses faster
Addressing modes
  RISC-V: Register, immediate, displacement (base+offset)
  Other examples: autoincrement, indexed, PC-relative
Types and size of operands
  RISC-V: 8-bit, 32-bit, 64-bit
Defining Computer Architecture

## Slide 11: Instruction Set Architecture
Operations
  RISC-V: data transfer, arithmetic, logical, control, floating point
  See Fig. 1.5 in text
Control flow instructions
  Use content of registers (RISC-V) vs. status bits (x86, ARMv7, ARMv8)
  Return address in register (RISC-V, ARMv7, ARMv8) vs. on stack (x86)
Encoding
  Fixed (RISC-V, ARMv7/v8 except compact instruction set) vs. variable length (x86)
Defining Computer Architecture

## Slide 12: Trends in Technology
Integrated circuit technology (Moore’s Law)
  Transistor density: 35%/year
  Die size: 10-20%/year
  Integration overall: 40-55%/year
DRAM capacity: 25-40%/year (slowing)
  8 Gb (2014), 16 Gb (2019), possibly no 32 Gb
Flash capacity: 50-60%/year
  8-10X cheaper/bit than DRAM
Magnetic disk capacity: recently slowed to 5%/year
  Density increases may no longer be possible, maybe increase from 7 to 9 platters
  8-10X cheaper/bit then Flash
  200-300X cheaper/bit than DRAM
Trends in Technology

## Slide 13: Bandwidth and Latency
Bandwidth or throughput
  Total work done in a given time
  32,000-40,000X improvement for processors
  300-1200X improvement for memory and disks
Latency or response time
  Time between start and completion of an event
  50-90X improvement for processors
  6-8X improvement for memory and disks
Trends in Technology

## Slide 14: Bandwidth and Latency
Log-log plot of bandwidth and latency milestones
Trends in Technology

## Slide 15: Transistors and Wires
Feature size
  Minimum size of transistor or wire in x or y dimension
  10 microns in 1971 to .011 microns in 2017
  Transistor performance scales linearly
    Wire delay does not improve with feature size!
  Integration density scales quadratically
Trends in Technology

## Slide 16: Power and Energy
Problem: Get power in, get power out
Thermal Design Power (TDP)
  Characterizes sustained power consumption
  Used as target for power supply and cooling system
  Lower than peak power (1.5X higher), higher than average power consumption
Clock rate can be reduced dynamically to limit power consumption
Energy per task is often a better measurement
Trends in Power and Energy

## Slide 17: Dynamic Energy and Power
Dynamic energy
  Transistor switch from 0 -> 1 or 1 -> 0
  ½ x Capacitive load x Voltage2
Dynamic power
  ½ x Capacitive load x Voltage2 x Frequency switched
Reducing clock rate reduces power, not energy
Trends in Power and Energy

## Slide 18: Power
Intel 80386 consumed ~ 2 W
3.3 GHz Intel Core i7 consumes 130 W
Heat must be dissipated from 1.5 x 1.5 cm chip
This is the limit of what can be cooled by air
Trends in Power and Energy

## Slide 19: Reducing Power
Techniques for reducing power:
  Do nothing well
  Dynamic Voltage-Frequency Scaling
  Low power state for DRAM, disks
  Overclocking, turning off cores
Trends in Power and Energy

## Slide 20: Static Power
Static power consumption
  25-50% of total power
  Currentstatic x Voltage
  Scales with number of transistors
  To reduce: power gating
Trends in Power and Energy

## Slide 21: Trends in Cost
Cost driven down by learning curve
  Yield
DRAM: price closely tracks cost
Microprocessors: price depends on volume
  10% less for each doubling of volume
Trends in Cost

## Slide 22: Integrated Circuit Cost
Integrated circuit
Bose-Einstein formula:
Defects per unit area = 0.016-0.057 defects per square cm (2010)
N = process-complexity factor = 11.5-15.5 (40 nm, 2010)
Trends in Cost

## Slide 23: Dependability
Module reliability
  Mean time to failure (MTTF)
  Mean time to repair (MTTR)
  Mean time between failures (MTBF) = MTTF + MTTR
  Availability = MTTF / MTBF
Dependability

## Slide 24: Measuring Performance
Typical performance metrics:
  Response time
  Throughput
Speedup of X relative to Y
  Execution timeY / Execution timeX
Execution time
  Wall clock time: includes all system overheads
  CPU time: only computation time
Benchmarks
  Kernels (e.g. matrix multiply)
  Toy programs (e.g. sorting)
  Synthetic benchmarks (e.g. Dhrystone)
  Benchmark suites (e.g. SPEC06fp, TPC-C)
Measuring Performance

## Slide 25: Principles of Computer Design
Take Advantage of Parallelism
  e.g. multiple processors, disks, memory banks, pipelining, multiple functional units
Principle of Locality
  Reuse of data and instructions
Focus on the Common Case
  Amdahl’s Law
Principles

## Slide 26: Principles of Computer Design
The Processor Performance Equation
Principles

## Slide 27: Principles of Computer Design
Principles
Different instruction types having different CPIs

## Slide 28: Principles of Computer Design
Principles
Different instruction types having different CPIs

## Slide 29: Fallacies and Pitfalls
All exponential laws must come to an end
  Dennard scaling (constant power density)
    Stopped by threshold voltage
  Disk capacity
    30-100% per year to 5% per year
  Moore’s Law
    Most visible with DRAM capacity
    ITRS disbanded
    Only four foundries left producing state-of-the-art logic chips
    11 nm, 3 nm might be the limit

## Slide 30: Fallacies and Pitfalls
Microprocessors are a silver bullet
  Performance is now a programmer’s burden
Falling prey to Amdahl’s Law
A single point of failure
Hardware enhancements that increase performance also improve energy efficiency, or are at worst energy neutral
Benchmarks remain valid indefinitely
  Compiler optimizations target benchmarks

## Slide 31: Fallacies and Pitfalls
The rated mean time to failure of disks is 1,200,000 hours or almost 140 years, so disks practically never fail
  MTTF value from manufacturers assume regular replacement
Peak performance tracks observed performance
Fault detection can lower availability
  Not all operations are needed for correct execution